## Slide 1
Planar® DirectLight™ LED Video Wall System
Processing Overview
August 2015

## Slide 2: Planar® DirectLight™ LED Video Wall System Content Planning
Video Processing Considerations
Content & Processing Options:
Design the content to fit the video wall’s resolution
Design the video wall to fit the content’s resolution
Use an external processor to process the content to fit the video wall

## Slide 3: Planar DirectLight Content Planning
Video Processing Considerations
Standard Resolution:
  If the Planar DirectLight video wall requires more than one LED Video Interface (LVI) at standard resolution, then each LVI must have its own content source. You may use either:
    An external video processor with one output to each LVI
    An PC with multiple graphics cards with one output to each LVI
    Multiple synchronized media players with one output to each LVI
Non-Standard Resolution:
  If the Planar DirectLight video wall requires more than one LED Video Interface (LVI) at non-standard resolution, then each LVI must have its own content source. You need:
    An external video processor with the ability to exactly match vertical refresh and pixel clock for all resolutions

## Slide 4: Example: Video Wall Equals One LVI
DL1.6: 8 x 6 LED Display Modules
1920 = 10.5’ (3.2m)
1080 = 5.9’ (1.8m)

## Slide 5: Example: Video Wall Equals One LVI
= 48 Modules
DL1.6: 8 x 6 LED Display Modules
1920 = 10.5’ (3.2m)
1080 = 5.9’ (1.8m)

## Slide 6: Example: Video Wall Equals One LVI
= 1 LVI
DL1.6: 8 x 6 LED Display Modules
1920 = 10.5’ (3.2m)
1080 = 5.9’ (1.8m)

## Slide 7: Example: Video Wall Equals One LVI
DL1.6: 8 x 6 LED Display Modules
LVI A
1920 x 1080
Processing Options
Media Player
PC
Synchronized Media Players
PC with multiple output video card
Video Processor
Video Processor that exactly matches vertical refresh and pixel clock for all resolutions
1920 = 10.5’ (3.2m)
1080 = 5.9’ (1.8m)

## Slide 8: Example: Video Wall Equals Two LVIs
DL1.6: 16 x 6 LED Display Modules
3840 = 21’ (6.4m)
1080 = 5.9’ (1.8m)

## Slide 9: Example: Video Wall Equals Two LVIs
DL1.6: 16 x 6 LED Display Modules
= 96 Modules
3840 = 21’ (6.4m)
1080 = 5.9’ (1.8m)

## Slide 10: Example: Video Wall Equals Two LVIs
DL1.6: 16 x 6 LED Display Modules
= 2 LVIs
3840 = 21’ (6.4m)
1080 = 5.9’ (1.8m)

## Slide 11: Example: Video Wall Equals Two LVIs
DL1.6: 16 x 6 LED Display Modules
LVI A
1020 x 1080
LVI B
1920 x 1080
Processing Options
Media Player
PC
Synchronized Media Players
PC with multiple output video card
Video Processor
Video Processor that exactly matches vertical refresh and pixel clock for all resolutions
3840 = 21’ (6.4m)
1080 = 5.9’ (1.8m)

## Slide 12: Example: Display Built to Match Video Wall (Non Standard Resolution)
3840 = 21’ (6.4m)
1,440 = 7.9’ (2.4m)
DL1.6: 16 x 8 LED Display Modules

## Slide 13: Example: Display Built to Match Video Wall (Non Standard Resolution)
= 128 Modules
3840 = 21’ (6.4m)
1,440 = 7.9’ (2.4m)
DL1.6: 16 x 8 LED Display Modules

## Slide 14: Example: Display Built to Match Video Wall (Non Standard Resolution)
= 4 LVIs
3840 = 21’ (6.4m)
1,440 = 7.9’ (2.4m)
DL1.6: 16 x 8 LED Display Modules

## Slide 15: Example: Display Built to Match Video Wall (Non Standard Resolution)
LVI C
1920 x 720
LVI D
1920 x 720
LVI A
1920 x 720
LVI B
1920 x 720
= 4x (1920 x 720)
3840 = 21’ (6.4m)
1,440 = 7.9’ (2.4m)
DL1.6: 16 x 8 LED Display Modules

## Slide 16: Example: Display Built to Match Video Wall (Non Standard Resolution)
DL1.6: 16 x 8 LED Display Modules
Processing Options
Media Player
PC
Synchronized Media Players
PC with multiple output video card
Video Processor
Video Processor that exactly matches vertical refresh and pixel clock for both resolutions
3840 = 21’ (6.4m)
1,440 = 7.9’ (2.4m)
LVI C
1920 x 720
LVI D
1920 x 720
LVI A
1920 x 720
LVI B
1920 x 720

## Slide 17: Example: Display Built to Match Vide Wall (Various Non Standard Resolutions)
DL1.6: 13 x 9 LED Display Modules
3120 = 17’ (5.2m)
1,620 = 8.8’ (2.7m)

## Slide 18: Example: Display Built to Match Video Wall (Various Non Standard Resolutions)
= 117 Modules
DL1.6: 13 x 9 LED Display Modules
3120 = 17’ (5.2m)
1,620 = 8.8’ (2.7m)

## Slide 19: Example: Display Built to Video Match Wall (Various Non Standard Resolutions)
DL1.6: 13 x 9 LED Display Modules
3120 = 17’ (5.2m)
1,620 = 8.8’ (2.7m)
LVI A (1680 x 900)
LVI B (1400 x 900)
LVI C (1680 x 720)
LVI D (1440 x 720)
= 4 LVIs of various resolutions
LVI C
1680 x 720
LVI D
1440 x 720
LVI A
1680 x 900
LVI B
1440 x 900

## Slide 20: Example: Display Built to Match Video Wall (Various Non Standard Resolutions)
Processing Options
Media Player
PC
Synchronized Media Player
PC with multiple output video card
Video Processor
Video Processor that exactly matches vertical refresh and pixel clock for all resolutions
LVI C
1680 x 720
LVI D
1440 x 720
LVI A
1680 x 900
LVI B
1440 x 900
DL1.6: 13 x 9 LED Display Modules
3120 = 17’ (5.2m)
1,620 = 8.8’ (2.7m)

## Slide 21: Example: Video Wall Smaller than One LVI
DL1.6: 4 x 6 LED Display Modules
960 = 5.3’ (1.6 m)
1080 = 5.9’ (1.8m)

## Slide 22: Example: Video Wall Smaller than One LVI
= 24 Modules
DL1.6: 4 x 6 LED Display Modules
960 = 5.3’ (1.6 m)
1080 = 5.9’ (1.8m)

## Slide 23: Example: Video Wall Smaller than One LVI
= 1 LVI
DL1.6: 4 x 6 LED Display Modules
960 = 5.3’ (1.6 m)
1080 = 5.9’ (1.8m)

## Slide 24: Example: Video Wall Smaller than One LVI
Processing Options
Media Player
PC
Synchronized Media Player
PC with multiple output video card
Video Processor
Video Processor that exactly matches vertical refresh and pixel clock for all resolutions
LVI
960 x 1080
DL1.6: 4 x 6 LED Display Modules
960 = 5.3’ (1.6 m)
1080 = 5.9’ (1.8m)

## Slide 25: Planar DirectLight Processing Selection Table
 |  | Media Player | PC | Synchronized Media Player | PC with multiple output video card | Video Processor | Video Processor that matches vertical refresh and pixel clock for all resolutions
LED video wall smaller than one LVI |  |  |  |  |  | ☻ | ☻
LED video wall equals one LVI |  | ☻ | ☻ | ☻ | ☻ | ☻ | ☻
LED video wall equals multiple LVIs with standard resolution |  |  |  | ☻ | ☻ | ☻ | ☻
LED video wall to match wall space, one or more non-standard resolutions |  |  |  |  |  |  | ☻

## Slide 26: Media Players
Best used for:
  Signage applications
  Standard resolution
  LED video wall driven by single LVI
  Content consist of one set of images or videos displayed across the entire video wall
  Definition:
  Purpose-designed appliance for the display of video and pictures
  Play, catalog and store art, photos and/or videos in resident hard drives or solid state storage
  On some models content can be managed over the network
  Low power consumption
  Rack-mountable, wall-mountable, table top and OPS configurations
  Available in HD and 4K resolutions

## Slide 27: Synchronized Media Players
Best used for:
  Signage Applications
  Standard resolution
  LED video wall driven by multiple standard resolution LVIs
  Content consist of one set of images or video displayed across the entire video wall
  Content consist of multiple images or video synchronized across different LVIs
  Definition:
  Purpose-designed appliance for the display of video and pictures
  Play, catalog and store local art, photos and videos in resident hard drives or solid state storage
  On some models content can be managed over the network
  Low power consumption processors
  Rack-mountable, wall-mountable, table top and OPS configurations
  Available in HD and 4K resolutions
  Players frame synchronized, allowing them to work together, creating a shared experience

## Slide 28: Personal Computers (PC)
Best used for:
  Running applications
  Standard resolution
  LED video wall driven by single standard resolution LVIs
  Content consist of one or various applications displayed across the entire wall
  Definition:
  Off-the-shelf computer with Windows, Mac or Linux operating systems
  Run applications from hard drive, network or internet
  With appropriate software, administrator can remote into PC for administrative purposes
  Recommended due ability to run custom and off-the-shelf applications
  Rack-mountable, wall-mountable, table top and OPS configurations
  Available in various resolutions

## Slide 29: Personal Computers (PC) with Advance Video Card
Best used for:
  Running applications
  Standard resolution
  LED video wall driven by multiple standard resolution LVIs
  Content consist of one or various applications displayed across the entire video wall
  Definition:
  Off-the-shelf computer with Windows, Mac or Linux operating systems
  Run applications from hard drive, network or internet
  With appropriate software, administrator can remote into PC for administrative purposes
  Recommended due ability to run custom and off-the-shelf applications
  Rack-mountable, wall-mountable, table top and OPS configurations
  Available in various resolutions
  Advanced graphics video card(s) allow connection to multiple LVIs (HDI)

## Slide 30: Video Processors
Best used for:
  Routing multiple sources into one or more video walls
  LED video wall driven by one or multiple non standard resolution LVIs
  Content consist of one or various sources or applications displayed across the entire video wall
Definition:
  Designed to enhance functionality of video walls
  Designed to capture, display and manage multiple sources on a video wall
  Supports wide range of visual inputs including analog, digital and high definition audio and computer sources
  Easy-to-use graphical user interface allows easy selection and placement of sources
  Run applications from hard drive, network or internet
  With appropriate software, administrator can remote into PC for administrative purposes
  Rack-mountable
  Professional graphics video card(s) allow connection to multiple LVIs (HDI inputs) outputs

## Slide 31: Video Processors (Exactly Match Vertical Refresh and Pixel Clock for all Resolutions)
Best used for:
  Routing multiple sources into one or more video walls
  LED video wall driven by one or multiple non standard resolution LVIs
  Content consist of one or various sources or applications displayed across the entire video wall
Definition:
  Designed to enhance functionality of video walls
  Designed to capture, display and manage multiple sources on a video wall
  Supports wide range of visual inputs including analog, digital and high definition audio and computer sources
  Easy-to-use graphical user interface allows easy selection and placement of sources
  Run applications from hard drive, network or internet
  With appropriate software, administrator can remote into PC for administrative purposes
  Rack-mountable
  Professional graphics video card(s) allow connection to multiple LVIs (HDI inputs) outputs
  Enhanced internal timing and set-up software to avoid video defects due to mixed resolutions

## Slide 32: Clarity® Visual Control Station™ (VCS™)
Add a resolution simply by entering the width, height and offset
When mixing 2 different resolutions, it automatically recalculates to the correct timing that exactly match vertical refresh and pixel clock for both resolutions
Avoids video imperfections (tearing) due to refresh frequency mismatch
Clarity VCS Optimizations Uniquely Matches Planar DirectLight Scalability

## Slide 33: Planar DirectLight background

## Slide 34: Planar DirectLight Video Connectivity
Planar DirectLight LED Video Interface:
Connects HDMI input to LED Display Modules
1920 x 1080 maximum resolution
Manages brightness and picture adjustments
Supports a RS-232 and LAN control
Resides behind the video wall
 | Maximum Width: | Maximum Height: | Maximum Total:
DL1.6 | 8 | 6 | 48
DL1.9 | 9 | 6 | 54
DL2.5 | 12 | 9 | 108
DL3.1 | 15 | 11 | 165
LED Display Modules are supported by a single LED Video Interface

## Slide 35
Planar DirectLight Content Planning (Standard vs. Non-Standard Resolutions)
Standard Resolutions:
Configuration supported by off-the-shelf video card drivers.
For example:
  1920 x 1080
  1600 x 900
  1280 x 720
  800 x 600
10.5’
3.2M
5.9’/1.8M
DL1.6: 144.5”/3.7M
1920*1080
Non-Standard Resolutions:
Configuration not supported by off-the-shelf video card drivers.
10.5’
3.2M
8.9’/2.7M
DL1.6: 144.5”/3.7M
1920*540
+1920*1080
= 1920*1620

## Slide 36: Examples: Non-Standard 16:9 Resolutions (In Red)
DL1.6 | 960x540 | 1,920x1,080 | 2,880x1,620 | 3,840x2,160
DL1.9 | 832x468 | 1,664x936 | 2,496x1,404 | 3,328x1,872
DL2.5 | 640x360 | 1,280x720 | 1,920x1,080 | 2,560x1,440
DL3.1 | 512x288 | 1,024x576 | 1,536x864 | 2,048x1,152
5.3’ 1.6M
10.5’ 3.2M
15.8’ 4.8M
21.0’ 6.4M
5.9’/1.8M
3.0’/0.9M
8.9’/2.7M
11.8’/3.6M
72.3”/1.8M
144.5”/3.7M
216.8”/5.5M
289.1”/7.3M